MAINTENANCE OF YOUR TRAILER

BEARINGS AND BRAKES

If the trailers is ever submersed in salt or fresh water the bearings will have to be stripped down to make sure no water has entered the bearings. If so the bearings MUST be cleaned using a suitable solvent. Repack the bearings with good waterproof grease. At this stage also check and clean the brakes and drum. Grease all brake linkages.

COUPLING

Grease the coupling through the grease nipple on top of the housing. Check the rubber Gaiter for any sign of damage. If damaged have it replaced.

CHASSIS

Always wash the chassis down with fresh water after it has been submersed in salt water.

NEVER PARK THE TRAILER FOR LONG PERIODS WITH THE HAND BRAKE ON.

When backing the trailer into a space apply the hand brake while it is still attached to the tow vehicle and drive forwards slowly 6 to 8 Inches to release the AUTOREVERSE MECHANISM inside the drum.

Chock the wheels and remove the Trailer from the tow ball; RELEASE THE HAND BRAKE. This will stop the brake shoes seizing to the drum.